## Slide 1: Electro-Optic Sampling Beam Positioning Monitor for Relativistic Electron Beams
North American Particle Accelerator Conference 2025
August 12, 2025
Elena L. Ros1, Michael L. Litos1, Alexander Knetsch2, Brendan O’ Shea2, Claire Hansel1, Daniel Matteo3, Gerdard Andonian3, Mark Hogan2, Robert Ariniello2, Shutang Meng1, Tara Hodgetts3, Valentina Lee1
[1] (CU Boulder, Physics), [2] (SLAC National Accelerator Laboratory), [3] RadiaBeam Technologies
Notes: Done

## Slide 2
U.S. Department of Energy, Office of Science, Office of High Energy Physics, under Award Number DE-SC001796.
National Science Foundation under Award Number PHY-1806053
and Faculty Early Career Development Program Award Number
PHY-2047083.
Our Research is Funded By…

## Slide 3
Motivation
Independent transverse and longitudinal measurement of drive and witness beam for Plasma Wakefield Acceleration (PWFA).
Require precise transverse alignment for emittance preservation.
Require precise longitudinal separation to minimize energy spread and maximize efficiency.
Non-destructive shot by shot measurement
PWFA Simulation
Witness Beam
Drive Beam
z

## Slide 4
EO Crystal
γ
e- beam
Laser
k
Background: EO Sampling
EO Spatial Encoding Scheme
Laser
k
EO Crystal
γ
e- beam
EO Crystal
γ
e- beam
Laser
k
EO Crystal
γ
e- beam
Laser
k
EO Crystal
γ
e- beam
Laser
k
Rotated Polarization
Temporal information mapped to transverse profile of laser1.

## Slide 5
Background: EO Sampling
k
Laser
Polarizer
Horizontally polarized
γ
e- beam
Polarizer
Vertically Polarized
Image on camera
Witness
Drive
CMOS Camera

## Slide 6
Electro Optic Sampling Beam Position Monitor
EOS BPM Mk.1
EO Crystal
Laser
EO Crystal
e- beam
Leverages correlation between strength of phase retardation and location of e- beam with respect to crystal2.

## Slide 7
EOS BPM Mk1. / Experimental Data
Beam position monitor for high intensity environments
Δx from DTOTR2 (μm)
Δx from EOS-BPM (μm)
EOS2 Drive Bunch Signal (arb)
EOS1 Drive Bunch Signal (arb)
Drive Bunch Δx at EOS-BPM inferred from DTOTR (μm)

## Slide 8
EOS BPM Mk.2 Design
4 Crystal Design
Axicon
e- beam
θ
EO Crystal
k
k
Tilted Pulse Front
Axicon creates circular donut
4 crystals around e- beam axis
More complete azimuthal coverage allows for position measurement in x and y.
Increase in total signal leads to better temporal and transverse resolution.
5o angle of incidence (θ)
3 ps temporal window
4 10mm x 10mm 100μm thick GaP wafers

## Slide 9
CAD Model/Pictures
Mounted 100μm Glass Wafers in EOS BPM Mk.2 Crystal Holder
e- beam

## Slide 10
EOS BPM Mk.2 Simulation
Parameter | Value | Unit
Laser Wavelength | 800 | nm
Laser Angle | 5 | degree
Drive Beam Charge | 1000 | pC
Witness Beam Charge | 800 | pC
Time Delay btw. Beams | 450/135 | fs/μm
Transverse Beam Offset Drive | ~10 | μm
Transverse Beam Offset Witness | ~10 | μm
Bunch Length (Both) | 50/15 | fs/μm
GaP Wafer Thickness | 100 | μm
t
Drive
Witness

## Slide 11
EOS BPM Analysis
α
e-beam
Intensity on Camera
Temporal window
θ is laser angle of incidence
r

## Slide 12
EOS BPM Analysis with Rotated Crystals
α1
e-beam
Intensity on Camera
Temporal window
θ is laser angle of incidence
α
α1 = α +π/2
Crystal rotated 90o
Crystal rotated 90o

## Slide 13
EOS BPM Mk.2 Time of Arrival Analysis

## Slide 14
EOS BPM Mk.2 Time of Arrival
SNR Drive Beam: 2.20
SNR Witness Beam: 0.92
SNR Drive Beam: 73.1
SNR Witness Beam: 50.4

## Slide 15
Time of Arrival with 1 crystal
SNR Drive Beam: 1.58
SNR Witness Beam: 0.74
SNR Drive Beam: 11.8
SNR Witness Beam: 4.9

## Slide 16
Study of Longitudinal Separation Resolution
Actual Bunch Separation | Fit
400 fs | 397 fs
405 fs | 402
410 fs | 407
415 fs | 412
420 fs | 418
425 fs | 422
430 fs | 428
~ 3 fs resolution with 15 % noise

## Slide 17
Study of Low Charge Bunches
Bunch Charge (pC) | Fit (fs) | Drive | Witness | Drive | Witness
800 | 447 | 19 | 12 | 450 | 350
700 | 447 | 14 | 9 | 300 | 230
600 | 447 | 11 | 7 | 260 | 200
500 | 447 | 7 | 4 | 190 | 150
400 | 448 | 5 | 3 | 120 | 100
300 | 448 | 3 | 2 | 80 | 70
200 | 450 | 1 | 1 | 50 | 50
100 | 440 | 0.5 | 0.1 | 35 | 35
Lineout SNR
Azimuthal Summing SNR
Actual: 450 fs
5% noise at 800pC

## Slide 18
EOS BPM Mk.2 BPM and TOA Results
3 fs TOA resolution
<5 μm transverse resolution

## Slide 19
Summary
Novel ultra-fast optical device for measuring beam centroid location with fs/μm level precision.
  Required for emittance preservation of PWFA.
  Required to minimize energy spread and maximize efficiency.
Expected Resolution:
  Longitudinal: ~ 3fs/1μm for signals with up to 40% noise.
  Transverse: < 5μm for signals with up to 40% noise.
Future Work:
  Install and commission EOS BPM Mk.2 at FACET-II next run.
  Explore the utility of EOS BPM to diagnose tilted beams.

## Slide 20
References
[1] A. L. Cavalieri et al., “Clocking Femtosecond X Rays,” Phys. Rev. Lett., vol. 94, no. 11, Mar. 2005, doi: 10.1103/physrevlett.94.114801.
[2] K. Hunt-Stone, R. Ariniello, C. Doss, V. Lee, and M. Litos, “Electro-optic sampling beam position monitor for relativistic electron beams,” Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, vol. 999, p. 165210, May 2021, doi: 10.1016/j.nima.2021.165210.
[3] S. Casalbuoni, H. Schlarb, B. Schmidt, P. Schmüser, B. Steffen, and A. Winter, “Numerical studies on the electro-optic detection of femtosecond electron bunches,” Phys. Rev. ST Accel. Beams, vol. 11, no. 7, Jul. 2008, doi: 10.1103/physrevstab.11.072802.
[4] B. Steffen et al., “Electro-optic time profile monitors for femtosecond electron bunches at the soft x-ray free-electron laser FLASH,” Phys. Rev. ST Accel. Beams, vol. 12, no. 3, Mar. 2009, doi: 10.1103/physrevstab.12.032802.

## Slide 21
Questions

## Slide 22
Signal Ringing for Short Bunches
Shorter electron bunches correspond to higher THz frequencies. For GaP the cutoff is ~ 10 THz due to the phase velocity mismatch.
This is better than ZnTe, but there is also the trade off, of lower signal.
The phase mismatch can cause ringing in the signal -> worse TOA resolution.
For FACET-II 100 μm GaP is optimal.

## Slide 23
Example of Ringing

## Slide 24
Single Crystal Signal

## Slide 25
Phase Retardation of Crystal
EO Crystal
e-beam
α
Signal from Phase Retardation

## Slide 26
Phase Retardation of Rotated Crystal Orientation
EO Crystal
e-beam
α
Signal from Phase Retardation
EO Crystal rotated 90o
αr
Ir
Ir
I
I

## Slide 27
BPM Analysis
Region I
Region II
Region I
α2
α1
r2
r1